MSW-12.1

12” High-Power Subwoofer

| SPECIFICATIONS |
| --- |
| Power Handling (RMS) | P | 400 W |
| Transient Power Handling |  | 1,500 watts |
| Sensitivity SPL @ 1watt | SPL0 | 90.8 dB |
| Nominal Impedance |  | 8 ( |
| Resonant Frequency | Fs | 23.3 Hz |
| VOICE COIL |
| Voice Coil Height |  | 30mm |
| DC Resistance | Revc | 6.2 ( |
| Zmax @ F0 | Z0 | 217.0 ( |
| MAGNET SYSTEM |
| Flux x Length | BL | 21.6 TM |
| Maximum Linear Excursion | Xmax | 10mm |
| Ref Efficiency | N0 | 0.76 % |
| OPERATIONAL PARAMETERS |
| Compliance | Cms | 377.3 (M/N |
| Mechanical Q Factor | Qms | 8.21 |
| Electrical Q Factor | Qes | 0.24 |
| Total Q Factor | Qts | 0.23 |
| Moving Mass | Mms | 123.4 grams |
| Diaphragm Mass | Mmd | 116.4 grams |
| Equivalent Cas Air Load | VAS | 150.5 Litres |
| Cone Material |  | polypropylene |
| Surround Material |  | santoprene( |
| Piston Area | Sd | 0.05 M2 |
| Dimensions | Diameter Cutout Height Mounting Depth |  | 315mm (12.4”) 283mm (11.1”) 156mm (6.1”) 140mm (5.5”) |
| Net Weight |  | 6.36 kg (14 lbs) |